## Slide 1: Reconfigurable Out-of-Order Mechanism Generator for Unstructured Grid Computation in Computational Fluid Dynamics
Dept. of Information and Computer Science, Keio Univ.
Takayuki Akamine, Kenta Inakagata, Hideharu Amano
Dept. of Electrical and Electronics Engineering, Ryukyu Univ.
Yasunori Osana
Aerospace Research and Development Directorate
Japan Aerospace Exploration Agency
Naoyuki Fujita
Notes: Thank you for the introduction, Mr. chairman.
Good Afternoon, I’m Takayuki Akamine from Keio University.
I would like to make the presentation about “reconfigurable out-of-order mechanism generator for unstructured grid computation in computational fluid dynamics”

## Slide 2: Agenda
Motivation
  CFD and FaSTAR,
  and Unstructured Grid
RAW hazards
Out-of-Order Mechanism
Evaluation
Conclusion
Notes: At first, I will talk about motivation of this work.

## Slide 3: Background
CFD(Computational Fluid Dynamics)
  Computer simulation for analyzing fluid behavior
  Design Tool for aircraft components such as engines and bodies
  Huge amount of computation
FaSTAR(FAST Aerodynamic Routines)
  A CFD package program developed by JAXA
  Adopts an unstructured grid for grid form
  Reaches a limit of acceleration by software parallel execution
FPGA acceleration
  Highly flexible to fit an algorithm
  A promising approach for accelerating FaSTAR
Notes: Computational Fluid Dynamics is one of scientific computing.
It is a helpful tool to analyze fluid behavior for designing aircraft components such as engines and bodies.
However, a CFD simulation requires a lot of time because of huge amount of computation.
In such application, there is FaSTAR, a CFD package program developed by JAXA
It adopts unstructured grid mesh for grid form data.
Unstructured grid is good at expressing a complicated shaped, and it saves labor for generating grid data.
According to JAXA’s report, FaSTAR reaches a limit of acceleration by software parallel execution.
Then, we investigate to accelerate FaSTAR with FPGAs.
FPGA has high flexibility, and adaptability for a certain algorithm.
Hardware tuning using an FPGA is a promising approach for accelerating FaSTAR.

## Slide 4: Related Work
Kentaro Sano, et al. [FCCM2007]
  A Systolic Architecture for Computational Fluid Dynamics on FPGAs
  Implementation of the fractional method
Hirokazu Morishita, et al. [FPT2008]
  Exploiting Memory Hierarchy for a Computational Fluid Dynamcis Accelerator on FPGAs
  Implementation of MUSCLE (Monotone Upstream-centered Schemes for Conservation Laws) in UPACS
Diego Sanchez-Roman, et al. [SPL2011]
  An Euler solver accelerator in FPGA for computational fluid dynamics applications
  Implementation of an Euler solver using unstructured mesh with Impulse C
In this work,
  Our target is a CFD package using unstructured grid
  In order to avoid the overhead of high-level synthesis, a HDL generator will be proposed
Notes: I will show you related work.
The first work is implementation of fractional method,
The second is implementation of MUSCLE in UPACS,
The third is implementation of an Euler solver using unstructured grid with high-level synthesis.
In the first and second work, target applications used structured grid.
In the third work, High-level synthesis used for implementation.
In this work,
Our target is a CFD package using unstructured grid
In order to avoid the overhead of High-level synthesis, HDL generator will be proposed

## Slide 5: Unstructured Grid
How to access unstructured grid
  Accessing a face, two contiguous grids sharing the face (cell-A, cell-B) are accessed
  Faces are accessed in ascending order
    Spatial locality of variables
  Each grid has different number of faces
    Irregular memory access
Q1
Q2
Q3
Q4
face: k
A
B
face: k+1
Ｆ
A
B
Ｆ
In FaSTAR, grid data has data locality,
but memory access has no regularity
Unstructured Grid
  It is good at expressing complicated shapes
  Grid data are generated automatically
Notes: Unstructured grid is different from structured grid because it does not placed regularly.
Unstructured grid is good at express complicated shapes.
Using unstructured grid, the grid data can be generated automatically.
Each application has its own method to access a grid.
In FaSTAR, faces are used to access grids.
Accessing a face, two contiguous grids sharing the face, named cell-A, and cell-B respectively, are accessed.
This is an example of unstructured grids.
If face-k is accessed, Q2 is accessed as cell-A, and Q1 is as cell-B.
As well as face-k, if face-k+1 is accessed, Q1 is cell-A, and Q4 is cell-B.
Additionally, faces are accessed in ascending order.
It means the variables has spatial locality.
Moreover, each grid has different number of faces.
This makes memory accesses irregular and unpredictable.
In FaSTAR, grid data has data locality, but memory access has no regularity.

## Slide 6: Agenda
Motivation
  CFD and FaSTAR,
  and Unstructured Grid
RAW hazards
Out-of-Order Mechanism
Evaluation
Conclusion
Notes: Here, I will explain a target problem: RAW hazard.

## Slide 7: RAW hazards
Block
RAM
read address
write address
read quantity
Synchronizer
Summation
address
RAW hazard is critical problem in FaSTAR
Floating-Point
Adder
updated quantity
1
1
1
2
2
3
4
4
d1
d2
d3
d4
d5
d6
d7
d8
d2
d3
d4
d5
d6
d7
d8
1
1
2
2
3
4
4
1
s1
d1
16-stage pipeline
s1’
Address FIFO
Quantity data FIFO
RAW hazards
wait for 16 clock cycles
can’t go to the pipeline
Notes: In FaSTAR, RAW hazards occur and degrade performance.
This diagram shows a part of solver in FaSTAR.
It calculates a total quantity value for each grid,
and BlockRAM has partial summation results.
Numbers in address FIFO are addresses for the BlockRAM.
I will show you how this diagram works.
At first, the first data whose address is “1” is inputted, and “s1” is obtained from BRAM,
and “s1” added to “d1”.
The floating-point adder has a 16-stage pipeline.
So, next data can’t go to the pipeline because “s1” is already used.
Next data should wait until “s1’” goes back to the same entry.
Thus, RAW hazards waste 15 clock cycles.
Moreover, unstructured grid makes it impossible to predict RAW hazards.

## Slide 8: Avoiding RAW hazards
Block
RAM
read address
write address
read quantity
Synchronizer
Summation
address
Floating-Point
Adder
updated quantity
1
1
1
2
2
3
4
4
d1
d2
d3
d4
d5
d6
d7
d8
d2
d3
d4
d5
d6
d7
d8
1
1
2
2
3
4
4
1
s1
d1
can’t go to the pipeline
Address FIFO
Quantity data FIFO
Not related to “s1”,
can go to the pipeline
RAW hazards would be avoided by changing the order of data
Data should be reordered dynamically
Notes: We considered how to reduce RAW hazards.
I will show you the same diagram.
As well, “s1” is accessed first.
When “s1” is processed in the floating-point adder, RAW hazards occur.
In this moment, data, whose address is “2”, is not related to “s1”,
and the data can go to the pipeline.
Due to the same reason, data, whose address is “3” or “4”, can go to the pipeline.
Thus, we think that RAW hazards would be reduced by reordering data,
and data should be reordered dynamically

## Slide 9: Goal of this work
Reducing hazards in 5 solvers
  Surface integral of flux(Surface)
  Green Gauss
  Summation of fluxes’ eigenvalue(Sum Eigen)
  Maximum of fluxes’ eigenvalue(Max Eigen)
  Coefficient Initialization(Coefficient)
An out-of-order(OoO) mechanism
An OoO mechanism generator
All suffer from RAW hazards
Notes: In this work, we would like to reduce hazards in 5 solvers which suffer from RAW hazards in FaSTAR computation:
Surface, Green Gauss, Sum Eigen, Max Eigen, and Coefficient.
Here, we would like to propose an out-of-order mechanism.
Although the mechanism is applied to each computation,
it is tiring to design the mechanism for each solver.
To avoid this work, the mechanism is generated automatically by using a generator program.

## Slide 10: Agenda
Motivation
  CFD and FaSTAR,
  and Unstructured Grid
RAW hazard
Out-of-Order Mechanism
Evaluation
Conclusion
Notes: Here, I will explain the out-of-order mechanism
including overview, architecture, behavior, and parameter.

## Slide 11: Overview
Changing the order of data dynamically so as to resolve data dependencies
Unlike common OoO mechanisms in general purpose CPUs†, the mechanism is devoted to single arithmetic unit
a
b
c
d
e
f
g
h
1
1
1
2
2
3
4
4
Address FIFO
Quantity data FIFO
OoO mechanism
Execution
Monitor
Waiting
Buffer
1
2
3
4
1
2
Holds data temporarily
Original order
Post-reordered
(ideal)
a
d
f
g
b
e
Shows which addresses are computed
†“ An Efficient Algorithm for Exploiting Multiple Arithmetic Units”,
Robert Tomasulo, IBM Journal of Research and Development(1967)
Notes: This is an overview of the out-of-order mechanism.
The mechanism changes the order of data dynamically so as to resolve data dependencies.
In this diagram, the data are inputted in this order.
Passing through the mechanism, the order of data is changed as this.
Unlike common out-of-order mechanisms in general purpose CPUs,
the mechanism is devoted to a single arithmetic unit, but the data are often vector.
The mechanism has two types of registers: an execution monitor and a waiting buffer.
The execution monitor shows which address is computed in the arithmetic unit.
With the information, it decides whether incoming data can go to the arithmetic unit or not.
If data cannot go to the arithmetic unit, the data are stored to the waiting buffer.
Stored addresses are compared with those in the execution monitor.

## Slide 12: Architecture
Assumption
4 stage-pipeline arithmetic
Two-dimensional vector quantity
Out-of-Order
mechanism
Arithmetic
Unit
Input
queue
≠?
≠?
≠?
≠?
≠?
≠?
≠?
≠?
comparators
4-entry
execution monitor
Pointer decides which entry would be updated
2×2 waiting buffer
Only the first element is compared
Notes: This is an example of architecture.
In this example, the arithmetic unit has a 4 stage-pipeline.
Two-dimensional quantity data will be processed.
Vector data are inputted sequentially.
That is, the first element of the vector is inputted at the first step, and the next is inputted in the second step.
Under this assumption, the out-of-order mechanism has a 4-entry execution monitor.
This pointer decides which entry would be updated, and move the next entry clock by clock.
Data from input queue is compared with all addresses in the execution monitor in every 2 clock cycles.
In this example, two by two waiting buffer is prepared.
A set of waiting buffer is composed with two buffers because of two-dimensional quantity.
Here, two sets of waiting buffer are prepared.
If incoming data cause RAW hazards, data should be stored into this waiting buffer.
Only the first element is compared with all entries in the execution monitor, and the second element follows it.

## Slide 13: Behavior
Out-of-Order
mechanism
≠?
≠?
≠?
≠?
≠?
≠?
≠?
≠?
comparators
Arithmetic
Unit
1
2
input
queue
0 clock
2 clock
4 clock
6 clock
8 clock
1
2
1
2
D
D
4
3
3
4
5
6
6
5
5
6
1
2
Recording addresses
same address
→ incoming data have to wait
Updated
→Processing finished
can go to the arithmetic unit
same address
→incoming data have to wait
Go to the arithmetic unit
10 clock
Assumption
4 stage-pipeline arithmetic
Two-dimensional vector quantity
Notes: This slides shows the behavior.
These numbers are addresses of BlockRAM,
and compared with those in the execution monitor.
At the 0th clock, data whose address is “1”, are inputted.
There is no same address in the execution monitor so that the arithmetic can process the input.
The data go to the arithmetic unit, and the addresses are recorded in the execution monitor.
At 2nd clock, there is still the same address in the execution monitor.
Thus, data should be stored to waiting buffer.
At 4th clock, new address arriving.
It can be inputted to the arithmetic unit directly.
Then the address in this boxes are overwritten by the incoming address.
This means that the first data finished being processed, and these data can be processed.
At 6th clock, new address is inputted.
These data are inputted to the arithmetic unit straightly.
At 8th clock, these data causes hazards, and should be stored in the waiting buffer.
Instead of incoming data, the stored data go to the arithmetic unit.

## Slide 14: Parameters
Parameterization supports us to generate various types of OoO mechanism
latency is set as same number of pipeline depth in an arithmetic unit
  latency decides the number of entries in an execution monitor
dimension is quantity vector dimension
set is the parameter decided by a designer
  “set×dimension” equals to the number of waiting buffer
Notes: In order to generate various types of OoO mechanism, the mechanism must be parameterized.
Main parameters decide the number of registers in an execution monitor and a waiting buffer.
Then, I’ll introduce main three parameters: latency, dimension, and set.
latency is set as same number of pipeline depth in an arithmetic unit.
latency is the parameter to decide the number of entries in an execution monitor.
dimension is quantity vector dimension
Set is the parameter which is decided by a designer.
Note that the product of dimension and set equals to the number of waiting buffer.

## Slide 15: Agenda
Motivation
  CFD and FaSTAR,
  and Unstructured Grid
RAW hazards
Out-of-Order Mechanism
Evaluation
Conclusion
Notes: Finally, I will talk about evaluation, and conclude this work.

## Slide 16: Evaluation Environment
FPGA ： Xilinx Virtex-4 XC4VLX100
Double-precision floating-point units based on IEEE754
Floating point units, BlockRAMs and FIFOs are generated by Xilinx CORE Generator
Synthesis ： Xilinx ISE 13.2
Test dataset ： grid data around 22,883 faces
computation | operation type | latency | dimension | Iteration
Surface | Adder | 16 | 5 | 1000
Green Gauss | Adder | 16 | 4 | 1000
Sum Eigen | Adder | 16 | 1 | 1000
Max Eigen | Comparator | 3 | 1 | 1000
Coefficient | Adder | 16 | 6 | 1
Table1. Parameters on each solver
Notes: Evaluation environment is shown as this slide.
Target FPGA is Xilinx Virtex-4 XC4VLX100.
This FPGA is rather old, but it is used in FLOPS-2D, which is reconfigurable accelerator we are exploiting.
As test data, we used grid data around 22,883 faces.
We applied the mechanism to five solvers in FaSTAR, where RAW hazards occur.
Parameters on each computations are shown here.
Only Max Eigen uses a comparator,
they have different dimension,
and only coefficient is iterated once.

## Slide 17: Hazards reduction
Increasing set reduced the number of RAW hazards
In most cases, hazards were eliminated when set is 2
Sum Eigen needed 7 sets for removal of hazards
graph1：the number of hazards with increasing set
Chart: the number of set(waiting buffer)
| non | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Surface | 22667.3333 | 5168.6667 | 551.1667 | 226.1667 | 128.6667 | 43.6667 | 66.5833 | 225.3333 | 302.4167 | 142.4167
Green Gauss | 22665.8462 | 7468.6154 | 548.3077 | 248.6154 | 105.2308 | 40.9231 | 57.8462 | 239.6923 | 302.4615 | 184
Sum Eigen | 22651 | 10345.3125 | 5752 | 3617.375 | 2336.75 | 1487.5 | 873.6875 | 428.9375 | 86 | 57.9375
Max Eigen | 22664 | 3920.3333 | 149.3333 | 67.6667 | 50.3333 | 50 | 92 | 78.6667 | 78.3333 | 64.3333
Coefficient | 22673.4545 | 476.3636 | 351.4545 | 198.1818 | 56.9091 | 58.5455 | 342.1818 | 197.0909 | 197.6364 | 57.4545
Notes: At first, we examined the relationship between the hazard reduction and the number of waiting buffer.
As this graph shows, increasing set reduced the number of hazards.
However, it might stretch critical path delay.
In most cases, when set is 2, hazards are eliminated enough.
Sum Eigen needs about 7 sets of waiting buffer for removal of hazards.
Since it uses scalar data, the penalty is worst in all solvers.
Fortunately, the delay is not so stretched in this solver,
and the hardware requirement is not so large.
So, we selected 8 sets for this solver.

## Slide 18: Acceleration evaluation
Software execution:
  Intel Core2Duo CPU(2.66GHz)
  Linux kernel ver2.6
  Intel Fortran Compiler 10.4
Chart: elapsed time(sec)
| software execution | In-order execution on an FPGA | OoO execution on an FPGA
Surface | 2.3 | 2.27 | 1.17
Green Gauss | 2.01 | 2.19 | 0.97
Sum Eigen | 1.59 | 1.75 | 0.26
Max Eigen | 1.59 | 0.44 | 0.199
Coefficient | 0.0016 | 0.00241 | 0.00129
2.88-fold speed-up with Intel Core2Duo CPU
2.55-fold speed-up with in-order execution on an FPGA
  6.7-fold speed-up in Sum Eigen
Notes: We examined the benefit of hazards reduction, and compared FPGA execution with CPU execution.
We compared out-of-order execution with in-order execution on FPGAs too.
Software execution is measured with this environment.
As shown in this picture, FPGA with the mechanism processed 2.88 times as fast as Intel Core2Duo.
The mechanism achieved 2.55-fold speed-up to in-order execution.
Sum Eigen, represented green box , is the most successful case because it suffers from critical penalty of hazards.
Using the mechanism, 6.7-fold speed-up is achieved compared with in-order execution.

## Slide 19: Resource Overhead
About 27% of resource overhead is required for peak performance on average
  The total overhead in an FPGA is 3.5% on average
Increase ratio of Sum Eigen is the biggest, but the impact of total resource is not so large
Computation | Slice usage (in-order) | Slice usage (on-peak) | Increase ratio | Occupation Increase
Surface | 10473 | 12889 | 23.1% | 4.91%
Green Gauss | 10528 | 12113 | 15.1% | 3.22%
Sum Eigen | 6215 | 9106 | 45.6% | 5.88%
Max Eigen | 3294 | 4149 | 26.0% | 1.73%
Coefficient | 10530 | 11617 | 24.6% | 2.21%
Notes: This table shows resource overhead on peak performance.
About 27% of resource overhead is required, and the total overhead in the FPGA is 3.5% on average.
Considering speed-up, it might be reasonable
Increase ratio of Sum Eigen is the biggest, but the impact of total resource is not so large
That is all about evaluation.

## Slide 20: Agenda
Motivation
  CFD and FaSTAR,
  and Unstructured Grid
RAW hazard
Out-of-Order Mechanism
Evaluation
Conclusion
Notes: Finally, I will talk about evaluation, and conclude this work.

## Slide 21: Conclusion
The out-of-order mechanism is applied to five solvers in FaSTAR
  In most cases, the hazards are eliminated when set is 2
  The mechanism achieved 2.88-fold speed-up to Intel Core2Duo,
  and 2.55-fold speed-up to in-order execution on an FPGA
Future work
  Evaluation should be done with various grid data sample
  Critical path delay should be reduced for further acceleration by using pipeline processing
Notes: In this work, we applied the out-of-order mechanism to five solvers in FaSTAR.
We examine stall reduction and acceleration.
In most cases, when set is 2, the stalls are eliminates.
On peak performance, the mechanism achieved 2.88 speed-up to Intel Core2Duo,
and 2.55-fold speed-up to in-order execution.
In future works, we should evaluates the mechanism with more grid data sample.
Critical path delay should be reduced for further acceleration by using pipeline processing.

## Slide 22: Thank you. Q&A
Notes: That’s all.
Thank you for your attention